## Slide 1
KTH Edge AI
Robotics Challenge
Kick-off meeting
2026.10.07
Notes: Good afternoon everyone, and thank you for joining the kick-off meeting. My name is Jingwei Dong. I am a postdoc of NSE department.
Today, I will first give you an overview of the challenge, explain the competition tasks, then introduce the robot platform and development environment, and finally go through the expected development timeline and next steps.

## Slide 2
Challenge overview
02
Each team will control a group of approximately four wheeled mobile robots operating in an unknown indoor environment. During the mission, the robots may need to:
Explore an initially unknown environment
Detect, identify, and localize different targets
Share information between robots and edge node
Allocate tasks among robots
Form robot groups to complete specific rescue tasks
Adapt their behavior according to mission updates
Manage computation, communication, or energy consumption
Core theme: AI + Robotics + Edge Computing + Communication + Control
Notes: Here is a brief overview of the challenge.
In this challenge, each team will work with a group of approximately four wheeled mobile robots operating in an initially unknown indoor environment. The overall scenario is inspired by search-and-rescue applications, where the robots need to explore the environment, identify targets, and then cooperate to complete different rescue tasks.
During the mission, the robots will need to build up information about the environment, detect and localize different targets, and share this information with each other and with the edge node.
Based on the current system state, the team will also need to decide how tasks should be allocated among the robots and, in some cases, how multiple robots should cooperate to complete one task.
Later in the challenge, the mission may also be updated, so the system should be able to adapt its behavior accordingly. At the same time, computation, communication, or energy consumption are also part of the overall system design.
So the challenge is not only about robotics. The main idea is to bring together AI, robotics, edge computing, communication, and control in one integrated multi-robot system.

## Slide 3
System architecture - overview
03
1. Mobile robot team
Robots perform sensing, local computation, motion control, and exploration.
Robots can communicate and share local information with each other.
2. Edge computing node
A single local computing server is available to each team.
Teams decide which tasks are executed onboard and which are offloaded to the edge.
Typical edge functions may include: multi-robot coordination; perception/object detection; map fusion; task allocation; LLM inference.
3. Human operator + LLM
The human operator provides natural-language mission updates.
The LLM interprets the instructions and converts them into executable tasks.
Notes: This is the overall system architecture of the challenge.
The system mainly consists of three parts: the mobile robot team, the edge computing node, and the human operator together with the LLM-based mission interface.
First, the robots are responsible for the local physical interaction with the environment. They perform sensing, local computation, motion control, exploration, and autonomous navigation. They can also exchange local information with each other when needed.
Second, each team will have access to one edge computing node. The edge node can be used as a shared computing and coordination platform. For example, teams may use it for multi-robot coordination, map or state aggregation, task allocation, perception, or other computation that they do not want to run directly onboard the robots.
We do not want to prescribe a fixed architecture here. Teams can decide what should run onboard the robots and what should be executed on the edge node.
Finally, in the LLM-guided part of the challenge, the human operator can provide high-level mission updates in natural language. The LLM then interprets these instructions and converts them into a form that can be used by the multi-robot system.
So, at a high level, the robots handle local sensing and execution, the edge node supports shared computation and coordination, and the operator provides high-level mission input.

## Slide 4
Competition environment
05
Illustrative arena
In-door, flat-floor environment of approximately 5m × 5m (final dimensions are TBD), containing rooms, walls, and static obstacles.
Rescue targets are represented by ArUco visual markers and divided into two types: Normal Targets and Cooperative Targets.
Rescue zone is used for rescue-completion verification. Each ArUco marker corresponds to one or more predefined Rescue Zones.
A rescue is completed when the robot enters the corresponding Rescue Zone and remains there continuously for the required duration.
Notes: This slide shows an illustrative version of the competition environment.
The arena will be an indoor, flat-floor environment of approximately five by five meters, although the exact dimensions are still to be finalized. The arena will contain rooms, walls, and several static obstacles.
The exact layout used in the competition will not be known to the teams in advance.
The rescue targets will be represented by ArUco markers. We consider two types of targets: Normal Targets and Cooperative Targets.
Each target is associated with one or more predefined Rescue Zones. For a Normal Target, there is one Rescue Zone. For a Cooperative Target, there are two Rescue Zones, because two different robots will need to cooperate to complete the task.
A rescue is considered complete when the required robot, or robots, enter the corresponding Rescue Zone and remain there continuously for a specified duration.
So the arena itself is relatively simple, but the main difficulty comes from exploring an unknown layout, detecting and localizing the targets, and then coordinating the robots to complete the rescue tasks.

## Slide 5
Overall competition flow
05
Task 1
Explore, map
and detect
Handover
Save unified
outputs
Task 2A
Autonomous
rescue
Safe Mode
Verify results and reposition
Task 2B
LLM-guided
mission
Two main tasks
Notes: This slide shows the overall competition flow. The challenge is divided into two main tasks.
In Task 1, the robots first explore the unknown environment, build a map, and detect and localize the rescue targets. At the end of Task 1, the team needs to save the outputs, including the map and the target information.
These outputs are then handed over to Task 2A, where the robots perform autonomous rescue based on the information obtained in Task 1. This is the main multi-robot coordination and rescue stage.
After Task 2A, the system enters a short Safe Mode. During this stage, the results are checked and the robots are repositioned to standardized starting positions for the next part, while the previously obtained map and target information are preserved.
Then we move to Task 2B, where an LLM-guided mission is introduced. The robots still use the same underlying multi-robot system, but the mission objectives and constraints are now provided through a natural-language instruction.

## Slide 6
Task 1 Autonomous exploration, mapping, and detection
06
Teams may use up to two robots starting from a designated start area to autonomously explore an unknown environment and build a unified 2D occupancy grid map within limited time:
The robot system shall operate autonomously based on the current map and sensor information, performing path planning, obstacle avoidance, and motion execution toward the selected target;
Existing ROS 2 SLAM, navigation, and other open-source software packages are allowed.
Notes: Now let’s look at Task 1 in more detail.
In Task 1, each team may use up to two robots. The robots start from a start zone and need to autonomously explore the initially unknown environment within a limited amount of time.
The main goal is to build a unified 2D occupancy-grid map of the arena. At the same time, the robots should also detect and localize the rescue targets they encounter during exploration.
One important point here is autonomy. The robots should make navigation decisions based on the current map and sensor information. This includes deciding where to go, planning a path, avoiding obstacles, and executing the motion without manual control.
Existing ROS 2 SLAM, navigation, and other open-source packages are allowed.
The challenge is more about how you integrate these components into a reliable autonomous exploration system.
If two robots are used, they should contribute to a common understanding of the environment and eventually produce one unified map and one unified target list.

## Slide 7
Task 1 Autonomous exploration, mapping, and detection
06
Teams may use up to two robots starting from a designated start area to autonomously explore an unknown environment and build a unified 2D occupancy grid map within limited time:
The robot system shall operate autonomously based on the current map and sensor information, performing path planning, obstacle avoidance, and motion execution toward the selected target;
Existing ROS 2 SLAM, navigation, and other open-source software packages are allowed.
Target detection and localization
The system shall perform the following pipeline:
01
ArUco observation
02
Identify target ID and type
03
Pose in
map frame
04
Update
target list
Estimate relative position
05
Required output: A 2D occupancy map and a target list
Notes: At the same time, robots also need to detect and localize rescue targets. We use ArUco markers for this purpose. The basic pipeline is shown here:
first observe the marker, then identify the target ID and target type, estimate its relative position with respect to the robot or camera, transform that pose into the global map frame, and finally update the shared target list.
So Task 1 has two main outputs. The first one is the unified 2D occupancy map, and the second one is the target list, which contains the detected targets and their locations in the map.
These outputs will be saved at the end of Task 1 and used directly in Task 2.

## Slide 8
Task 2A Multi-robot rescue
08
Task 2 uses the unified map and target list generated in Task 1. Multiple robots cooperate to complete rescue tasks. Teams may use up to four robots and use the organizer-provided edge node for global state aggregation, task planning, and multi-robot coordination.
Task 1 Outputs
Unified Map
ID Type
T1 Normal
TC1 Coop.
Target List
Map + target information from Task 1
Edge Node
Task assignments
State / progress
Task planning – What should be done next?
Robot allocation – Which robot(s) should do it?
Coordination – How should robots cooperate?
Global state – Track progress and update plans
Multiple Robots
Autonomous Navigation & Rescue Execution (path planning, motion control, obstacle avoidance)
Design the robot–edge communication interface
Build global robot and target state management
Develop task planning and robot allocation
Teams develop
Implement multi-robot coordination
Integrate task assignments with autonomous navigation and rescue execution
Notes: Now we move to Task 2A, which is the multi-robot rescue stage.
Task 2A starts from the outputs generated in Task 1, mainly the unified map and the target list. Based on this information, the team can use up to four robots to complete the rescue tasks.
The edge node acts as the main shared coordination platform. It collects the current robot and target states, keeps track of the global mission progress, and supports task planning, robot allocation, and multi-robot coordination.
For example, the system needs to decide which target should be handled next, which robot or robots should be assigned to that target, and, for cooperative targets, how different robots should coordinate with each other.
The edge node then sends task assignments to the robots. The robots themselves execute the assigned tasks through autonomous navigation, including path planning, obstacle avoidance, and motion control.
At the same time, they continuously send their state and task progress back to the edge node, so the global plan can be updated when necessary.
From the team-development perspective, you are expected to build this integration layer. This includes designing the robot–edge communication interface, maintaining global robot and target states, developing the task-planning and robot-allocation strategy, implementing multi-robot coordination, and connecting the high-level task assignments to autonomous navigation and rescue execution.

## Slide 9
Normal and cooperative rescue
09
Normal Target
Cooperative Target
Rescue Zone
Zone A
Zone B
1 robot
Continuous dwell
2 different robots
Simultaneous continuous dwell
Rescue zone position is determined from the marker pose using unified and publicly specified geometric rules (TBD)
Task 2A is also time-limited and ends when one of the following conditions occurs: (1) The competition time limit is reached; (2) All valid rescue targets have been successfully completed; (3) The referee terminates the run due to safety, equipment failure, or another necessary reason.
After Task 2A results have been verified, the organizers will reposition the robots to predefined Task 2B starting positions. The map, target list, and other environment information obtained previously are retained.
Notes: As mentioned before, in Task 2A, we consider two different types of rescue targets: Normal Targets and Cooperative Targets.
For a Normal Target, one robot needs to enter the corresponding Rescue Zone and remain there continuously for the required dwell time.
For a Cooperative Target, two different robots are required. Each robot must occupy one of the two predefined rescue zones, Zone A and Zone B, and both robots need to satisfy the dwell condition at the same time. The cooperative rescue is only completed when both robots are simultaneously in position for the required duration.
The rescue-zone locations will be determined from the ArUco marker pose using a unified geometric rule.
Task 2A is also time-limited. It ends when the time limit is reached, when all valid rescue targets have been completed, or when the referee terminates the run for safety or technical reasons.
After Task 2A, we will verify the results and reposition the robots to predefined starting positions for Task 2B. The map, target list, and previously obtained environment information are retained.

## Slide 10
Task 2B LLM-guided mission: Task flow
11
In this task, the LLM acts as a high-level mission interpreter and planner. Its primary role is to understand the natural-language mission instruction and convert mission objectives and high-level constraints into a structured mission plan.
Edge Node
Task assignments
State / progress
Multiple Robots
Autonomous Navigation & Rescue Execution
Operator
Natural-language mission input
LLM Mission Interpreter
Interpret instruction，Extract objectives & constraints， Generate a structured mission plan
Multi-Robot Coordinator
Execution planning ，Robot allocation，Coordination，
Global state management
Structured mission plan
Natural-language mission input interface
LLM prompting and mission interpretation
Structured mission-plan representation
Teams develop
Integrate the LLM mission layer with the existing Task 2A coordination framework
Retained
information
Notes: Task 2B builds directly on top of the Task 2A framework.
The main new element is the LLM-based mission interpretation layer. Instead of using only a predefined rescue objective, the operator now provides a natural-language mission instruction.
For example, the instruction could specify which target should be rescued first, which targets may be handled in parallel, or which target must be completed last.
The LLM running on the edge node interprets this natural-language instruction, extracts the mission objectives and high-level constraints, and converts them into a structured mission plan.
This structured mission plan is then passed to the same multi-robot coordinator that was already used in Task 2A. The coordinator is still responsible for execution planning, robot allocation, coordination, and global state management.
The robots themselves still perform autonomous navigation and rescue execution.
From the team side, the additional work is mainly to build the natural-language mission interface, design the LLM prompting and mission interpretation process, define a structured mission-plan representation, and integrate this LLM layer with the existing Task 2A coordination framework.

## Slide 11
Task 2B LLM-guided mission: Task flow
11
In this task, the LLM acts as a high-level mission interpreter and planner. Its primary role is to understand the natural-language mission instruction and convert mission objectives and high-level constraints into a structured mission plan.
Edge Node
Task assignments
State / progress
Multiple Robots
Autonomous Navigation & Rescue Execution
Operator
Natural-language mission input
LLM Mission Interpreter
Interpret instruction，Extract objectives & constraints， Generate a structured mission plan
Multi-Robot Coordinator
Execution planning ，Robot allocation，Coordination，
Global state management
Structured mission plan
Retained
information
Simple Example
Natural-language mission
“Rescue T2 first. Then T1 and T3. Complete TC1 last.”
LLM → Structured mission plan
T2 → {T1, T3} → TC1
Coordinator / Robots
Robot assignment, navigation, coordination and rescue execution
Notes: Here is a simple example of how the LLM-guided mission works.
Suppose the operator gives the instruction: “Rescue T2 first. Then rescue T1 and T3. Complete TC1 last.”
The LLM interprets this instruction and converts it into a structured mission plan.
The coordinator then uses this structured plan to decide the actual robot assignments and execution sequence. The robots still handle navigation, coordination, and rescue execution in the same way as in Task 2A.
So the LLM provides the mission-level logic, while the coordinator and robots carry out the mission.

## Slide 12
Robot platform and development environment
04
The competition uses differential-drive wheeled mobile robots:
Differential-drive platform
Wheel encoders
Mobile Base
Perception
RPLIDAR — mapping & obstacle sensing.
RealSense D435i — RGB-D perception & ArUco detection
State Estimation
Wheel encoders
IMU
Odometry/localization support
Onboard Computing
Intel NUC11TNKi5
NVIDIA GT 1030
ROS 2 onboard software
More information about the robot can be found at: https://canvas.kth.se/courses/59505/pages/robot-setup?module_item_id=1339720
Edge node information to be announced later…
Notes: Now I would like to briefly introduce the robot platform that will be used in the challenge.
The competition uses differential-drive wheeled mobile robots. Each robot is equipped with wheel encoders and an onboard computer and sensors including RPLIDAR for mapping and obstacle sensing, and a camera used for marker detection.
More detailed information about the robot hardware is available through the KTH course material shown here.
The exact hardware specification and runtime environment of the edge node are still being finalized, and we will announce those details later.

## Slide 13
Robot platform and development environment
04
Environments used to develop, test, integrate, and deploy the challenge system:
1. Robot & Edge computing
• Ubuntu Linux
• ROS 2
• Python / C++
• ROS 2 workspace & package system
Provides the common runtime and development environment for robot-side and edge-node applications.
2. Simulation environment
• Gazebo
• Simulated robot model
• Simulated indoor competition arena
• Simulated LiDAR/RGB-D sensors
Enables autonomy and multi-robot behaviors to be developed and tested before physical deployment.
3. Communication environment
• Local Wi-Fi/LAN
• ROS 2 DDS communication
• Topics / services / actions
• Robot IDs and namespaces
Supports communication between robots, the edge node, and the operator, including task dispatching, state sharing, feedback, and coordination.
4. Development & Debugging
• RViz
• ROS 2 CLI & colcon
• rosbag
• Git / VS Code / terminal tools…
Supports visualization, debugging, data recording, software integration, and team collaboration.
Task 2B add-on: LLM inference runtime and model on the edge node — exact backend/model to be specified later.
Notes: This slide summarizes the common development environment that will be used throughout the challenge. I will not go into details here, because these are quite standard robotic systems development tools.
For Task 2B, we also plan to provide an LLM inference runtime on the edge node, but the exact backend and model are still being finalized and will be announced later.

## Slide 14
What we provide vs. What teams develop
Organizer Provides
Teams Develop
Status:
Available
Partial
To do
Available
Robot platform & onboard hardware
Available
ROS 2 / Gazebo development environment
Available
Basic robot model for Gazebo simulation
Available
Simulated sensor / Single-robot SLAM baseline
Partial
Basic setup/ simulation tutorial
Partial
Competition task/ arena / target specification
Real-robot ROS 2 I/O interface
Robot-edge basic network connectivity
To do
Edge-node base runtime / LLM environment
• Autonomous exploration and navigation integration
• Target detection and localization
• Robot–edge communication and information sharing
• Global robot / target / task-state management
• Task planning and robot allocation
• Multi-robot coordination and cooperative rescue
• Feedback, failure handling, and replanning
• LLM mission interpretation and integration for Task 2B
• Overall system integration and testing
To do
To do
Notes: This slide clarifies the boundary between what the organizers will provide and what each team is expected to develop.
On the left, you can see the current status of the organizer-side baseline. Some parts are already available. For example, the robot platform and onboard hardware are ready, the ROS 2 and Gazebo development environment is available, and we already have a basic robot model for simulation.
Some other parts are still being completed. These include the basic setup and simulation tutorial, as well as the final competition task, arena, and target specifications.
There are also several items that are still to be finished before the full development phase starts, such as the real-robot ROS 2 I/O interface, the basic network connectivity between the robots and the edge node, and the base runtime environment for the edge node and the LLM.
The right-hand side shows the main parts that each team is expected to develop.
This includes autonomous exploration and navigation integration, target detection and localization, robot–edge communication and information sharing, global robot and task-state management, task planning and robot allocation, and multi-robot coordination.
Teams will also need to handle feedback, failures, and replanning, and for Task 2B, integrate the LLM-based mission interpretation layer.
Finally, the whole system needs to be integrated and tested as one complete multi-robot solution.

## Slide 15
Milestone and development timeline
13
End-to-end autonomous rescue baseline (simulation demo is sufficient)
Autonomous exploration, ArUco detection and localization
Autonomous map-based navigation
At least two robots should connect, with their states available to the system
Basic robot–edge communication demonstrated
Basic task planning and robot allocation
At least one Normal Rescue and one Cooperative Rescue
Week 0
Kick-off
Week 4
Mid-term milestone
Week 8
Final
Early Development Phase
Integration and real-robot validation
• Focus primarily on Gazebo simulation
• Develop and test exploration, SLAM, navigation, multi-robot coordination…
• Use simulation for rapid iteration and debugging
• Physical robots are used mainly for validation and system integration
• Teams that need real-robot testing should book a time slot in advance
Notes: This slide shows the development timeline and the mid-term milestone.
We currently plan an eight-week development period, with one main milestone around Week 4.
The purpose of this milestone is to check whether each team has established a working end-to-end autonomous rescue baseline.
For the milestone, a simulation demo is sufficient.
We expect teams to demonstrate autonomous exploration, marker detection and localization, autonomous map-based navigation, and at least one Normal Rescue and one Cooperative Rescue.
We would also like to see that at least two robots can be represented in the system, with their states available, and that some basic robot–edge communication has been established, for example the edge node being able to receive robot-state information. And achieve basic task planning and robot allocation.
During the first half of the development period, we strongly recommend that teams focus mainly on the Gazebo simulation environment. This is the best place to develop and debug exploration, SLAM, navigation, target detection, and the first version of multi-robot coordination.
After the mid-term milestone, the focus should gradually move toward system integration and real-robot validation. The physical robots are mainly intended for validation rather than being the primary development platform.
Because the number of physical robots and testing slots is limited, teams that need real-robot testing should book a time slot in advance. Ideally, you should already have a working simulation baseline before coming to the hardware test.

## Slide 16
Resources and next steps
14
Resources
Rulebook v0
Robot Setup and Technical Tutorial
ROS 2 workspace and Gazebo resources
After this meeting
1 Set up and run the simulation
2 Check interfaces and SLAM
3 Implement autonomous exploration
4 Assign team responsibilities
Questions and discussion
Notes: Finally, I would like to summarize the resources and the immediate next steps after this meeting.
We will provide the initial version of the rulebook, the robot setup and technical tutorial, as well as the ROS 2 workspace and Gazebo resources. Some of these materials are still being refined, so please treat the current rulebook as an initial version, and we will update the details as the challenge progresses.
After this meeting, the first thing I recommend is to set up and run the simulation environment successfully. Then, check the available robot interfaces and the SLAM baseline, and make sure you understand how the basic system works.
After that, you can start implementing autonomous exploration and, within your team, divide the responsibilities for different parts such as perception, navigation, communication, coordination, and system integration.
The main goal at this stage is not to solve everything immediately, but to get the basic development environment running and establish a clear team structure and technical plan.
That is all from my side for today. Thank you again for joining, and now we can move to questions and discussion.